## Slide 1
RescueForge
CAD to DIN 14095 Fire Safety Plans — Powered by AI
Siemens Hackathon 2025 | Industrial AI Track
v0.5.0

## Slide 2
The Challenge
Fire departments need standardized orientation plans (DIN 14095 / FKS) for every building. Creating these manually from CAD drawings is time-consuming, error-prone, and requires specialized knowledge.
Manual Process
Hours of work per floor plan
Expert Required
DIN 14095 knowledge needed
Error-Prone
Missing symbols, wrong colors

## Slide 3
Our Solution
Step 1
Upload
DWG/DXF building plan
Single or batch upload
Step 2
AI Processes
Automatic cleanup, room
detection & classification
Step 3
DIN 14095 Plan
FKS-compliant SVG + PDF
with all required symbols
→
→

## Slide 4
Processing Pipeline
10-step automated pipeline from CAD to DIN 14095 plan
DWG
Convert
ODA
→
DXF
Parse
ezdxf
→
Unit
Detect
Heuristic
→
Room
Detect
Shapely
→
AI
Classify
Gemini
Corridor
Route
Voronoi
→
SVG
Generate
svgwrite
→
Symbol
Place
Collision
→
PDF
Export
WeasyPrint
→
Suppl.
Docs
Cover+Sit
↓

## Slide 5
AI-Powered Room Classification
How It Works
1. Floor plan rendered as PNG with numbered rooms
2. Image sent to Vision API (Gemini 2.5 Flash)
3. AI returns room type + label for each room
4. Automatic retry (3x) on API failure
5. Heuristic fallback if AI unavailable
17 Room Types
Office, Corridor, Stairwell
Elevator, Bathroom, Kitchen
Storage, Technical, Server Room
Garage, Lobby, Conference
Residential, Bedroom, Living Room
Balcony, Unknown

## Slide 6
DIN 14095 / FKS Compliance
Filled Walls
Double-line polygons
RAL 9004 Signalschwarz
Fire Walls
RAL 3000 Feuerrot
2x normal thickness
18 FKS Symbols
DIN 14034-6 compliant
Smoke, call, exits, etc.
Escape Routes
Corridor centerline routing
Voronoi + NetworkX
DIN Title Block
ISO 7200 layout
Scale, date, references
Color Coding
RAL standard colors
Green corridors, red fire

## Slide 7
Key Algorithms
Voronoi Medial Axis
SciPy Voronoi on corridor boundary points. Filter ridges inside polygon to extract centerline for escape routes.
Unit Auto-Detection
Try all unit conversions, pick one giving 5-500m building size. Corrects wrong $INSUNITS headers.
Symbol Collision Avoidance
AABB overlap detection with 4-direction shift. Label-aware placement prevents overlapping in small rooms.
Door Deduplication
Merge arc + layer + INSERT + wall-gap detections. Sort by position, merge within tolerance, prefer standard widths.

## Slide 8
Tech Stack
Backend
Python 3.12 + FastAPI
ezdxf (CAD parsing)
ODA File Converter (DWG)
Shapely + STRtree (geometry)
SciPy Voronoi + NetworkX
OpenRouter API (Gemini 2.5 Flash)
svgwrite + WeasyPrint
ThreadPoolExecutor + JobStore
Frontend & Infrastructure
Next.js 15 + React 19
Tailwind CSS + lucide-react
WebSocket + HTTP polling fallback
Cypress E2E tests
Docker Compose (non-root)
GitHub Actions CI/CD
Coolify deployment
EN/DE i18n (localStorage)

## Slide 9
Features
Interactive Room Editor
Reclassify rooms, regenerate plans instantly
Batch Upload
Process multi-floor buildings at once
Real-Time Progress
WebSocket updates with auto HTTP fallback
Multi-Language
Full EN/DE support, German as default
Comparison View
Side-by-side original DXF vs FKS plan
Complete Plan Set
Floor plan + cover sheet + situation plan + compliance report

## Slide 10
Testing & Quality Assurance
328+
Backend Tests
19
Test Suites
E2E
Cypress Tests
Test Category | Coverage
Plan Generator (50 tests) | SVG output, DIN title block, walls, fire features, escape routes, languages
DXF Parser (39 tests) | Layer classification, multilingual (EN/DE/FR/ES/VI), fire safety patterns
Visual Regression (24 tests) | SVG fingerprint baselines + CairoSVG pixel-based comparison (7 scenarios)
API Routes (44 tests) | Upload, batch, status, download, metrics, room update, error endpoints
Corridor Routing (8 tests) | Voronoi medial axis, corridor graph, NetworkX pathfinding

## Slide 11
Performance & Architecture
Chart: Pipeline Duration (~12s total)
| DXF Parse | Room Detect | AI Classify | SVG Generate | PDF Export | Supplementary
Duration (ms) | 500 | 300 | 5000 | 100 | 2000 | 20
2-Service Architecture
Frontend (Next.js 15)
Port 3000
↕ HTTP/WS
Backend (FastAPI)
ThreadPool + JobStore
Docker Compose | Non-root | Coolify Deploy

## Slide 12
Security & Reliability
Security Headers
X-Content-Type-Options, X-Frame-Options, CSP, Referrer-Policy
Rate Limiting
20 req/60s per IP on upload endpoints, auto memory cleanup
Input Validation
Only .dwg/.dxf accepted, UUID job IDs, room type enum checks
CORS Configuration
Configurable origins, credentials only with explicit origins
Error Persistence
Detailed error.json on failure with step, elapsed time, error type
Non-Root Containers
Production-hardened Docker with dedicated app user (UID 1000)

## Slide 13
Hackathon Deliverables
Working prototype (Docker Compose, live at resuceforge.skimu.de)
AI-powered room classification (Gemini 2.5 Flash Vision API)
DIN 14095 / FKS-compliant plan output (SVG + PDF)
Complete plan set: Floor plan + Cover sheet + Situation plan + Compliance report
Interactive room editor with live regeneration
Batch upload for multi-floor processing
328+ automated tests (19 suites) + Cypress E2E
CI/CD pipeline (GitHub Actions)
Multi-language support (EN/DE)
Corridor-centerline escape routes (Voronoi + NetworkX)
Symbol collision avoidance + fire safety element recognition
DIN-standard scale detection (1:50 to 1:1000)

## Slide 14
RescueForge
From CAD to Fire Safety Plan in Seconds
github.com/NWichter-NeoTube/RescueForge
resuceforge.skimu.de
Siemens Hackathon 2025 | Industrial AI Track